## Slide 1
Final presentation
Master’s research project
Design, Implementation, and Evaluation of an Automotive Experimental Platform for Autonomous
Cooperative Adaptive Cruise Control (CACC)

## Slide 2: Outlines
Introduction
Background
Building The Platform
Platform Performance Analysis and Summary
Conclusion and Future Improvements

## Slide 3: Introduction
Personal Information
Objective and Motivation
Research Questions
Goals
Objective:
  Build an experimental model for Autonomous Vehicles Platooning
Motivation:
  Why do we need such a testbed?
  What is the type of our research topic?
  What should be done in order to bring our implementation to the real world?

## Slide 4: Introduction
Personal Information
Objective and Motivation
Research Questions
Goals
Is it possible to build a small-scale testbed giving the provided funds?
Will this model produces useful –close to real-world- results?
Is it possible to control and monitor the platform and extract data from it?
Does that model have the capability to test different platooning techniques in terms of control and communication strategies?
Notes: Which track and vehicles should be used as a Model? Are the hardware components going to fit inside the vehicle?
Which controller is better in terms of cost and efficiency? Does it supports Real-Time Operating System?
How to structure the software code and software layers?
Which building system shall be used?
Which communication modules and protocol can match the given requirement?
What measurements should be done? and what sensors are more suitable and should be used?
How to log data in order to be analyzed?
How to achieve remote control over the model?
What verification steps should be applied for each component of implemented
software and hardware?

## Slide 5: Introduction
Personal Information
Objective and Motivation
Research Questions
Goals
1. A well-constructed and designed platform that can be used as a testbed (i.e., vehicles and road emulation).
2. Equipped with accurate sensors with proper sampling frequency.
3. Stable communication.
4. Real-time and efficient controller.
5. Additional features.
Notes: 1.1. Track should have a sufficient length and reliable shape.
1.2. Vehicles should be able to carry electronics and can be easily controlled on the track with the least effort.
________________________________________
3.1. Able to provide different communication and message passing schemes.
3.2. Preserve the Cooperative Awareness Message (CAM) refresh rate.
3.3. Works with minimum packet loss.
________________________________________
3.4. Deterministic communication behavior.
________________________________________
4. Real-time and efficient controller.
4.1. High controller frequency, to preserve the required control update rate.
4.2. Real-time software using Real-Time Operating System.
4.3. Atomic execution for critical sections (e.g., measuring relative distance)
________________________________________
5.1. Remote control and monitoring.
5.2. Multiple communication protocols such as ZigBee, & Wi-Fi, and Low Energy Bluetooth (BLE) to enable further research.
5.3. Data logging for post-processing analysis.

## Slide 6: Background
Birds platoon[1]
Flight jets platoon[2]
Flight jets platoon[3]
Vehicles platoon[4]
Trucks platoon[5]
Combined platoon[5]
Autonomous Platooning
Adaptive Cruise Control
Cooperative Adaptive Cruise Control
Control Methods
Wireless Communication
Notes: https://www.reddit.com/r/enlightenedbirdmen/comments/7qh831/my_new_platoon_chep/
https://texasnewstoday.com/russian-military-aircraft-are-practicing-bombing-enemy-ships-during-training-in-the-black-sea/344930/
https://www.merriam-webster.com/words-at-play/origin-of-squadron-and-squad
https://www.tech-faq.com/vehicle-platooning.html
https://erticonetwork.com/large-scale-deployment-of-multi-brand-truck-platooning-on-european-roads/

## Slide 7: Background
Autonomous Platooning
Adaptive Cruise Control
Cooperative Adaptive Cruise Control
Control Methods
Wireless Communication
Stop & Go cruise control
Speed limit-aware cruise control
Eco cruise control for fuel and EV capacity savings
Cruise control in curves
Turn-by-turn cruise control
Predictive adaptive cruise control
Parking speed control
Dynamic priority cruise control
ACC demonstration[6]
ACC Types[7]
Notes: https://www.zf.com/products/en/cars/products_30982.html
b

## Slide 8: Background
CACC demonstration[8], [9]
Autonomous Platooning
Adaptive Cruise Control
Cooperative Adaptive Cruise Control
Control Methods
Wireless Communication
Notes: https://www.aimsun.com/de/technische-hinweise/modellierung-verbundener-fahrzeuge-mit-aimsun-api/
Stephen Jones, N. Wikström, A. Ferreira Parrilla | DS | 29 November 2018 - Energy-Efficient Cooperative Adaptive Cruise Control (EECACC)

## Slide 9: Background
Autonomous Platooning
Adaptive Cruise Control
Cooperative Adaptive Cruise Control
Control Methods
Wireless Communication
String stability
longitudinal control strategy.
Introduces the amplification of the spacing error among a string of vehicles (platoon).
Tries to attenuate spacing error.
It requires knowledge and data about more than the preceding vehicle
Notes: https://www.aimsun.com/de/technische-hinweise/modellierung-verbundener-fahrzeuge-mit-aimsun-api/
Stephen Jones, N. Wikström, A. Ferreira Parrilla | DS | 29 November 2018 - Energy-Efficient Cooperative Adaptive Cruise Control (EECACC)

## Slide 10: Background
Autonomous Platooning
Adaptive Cruise Control
Cooperative Adaptive Cruise Control
Control Methods
Wireless Communication
Wireless Communication
Cooperative Awareness Message (CAM)
Specification:
  Data rate
  Packet loss
  Delay
  Behavior
Communication topology?
  (e.g., Mesh topology)
Available options?
  (e.g, Wi-Fi, Bluetooth, BLE, and ZigBee)
CAM message
Velocity
Time stamp (s)
Displacement
Acceleration
Target Velocity
Target Acceleration
Target Distance
Time stamp (micro-seconds)

## Slide 11: Background
Autonomous Platooning
Adaptive Cruise Control
Cooperative Adaptive Cruise Control
Control Methods
Wireless Communication
Accurate measurements for preceding vehicle relative distance, velocity
and acceleration.
Accurate measurements for the i_th vehicle displacement, velocity and acceleration.
Preserve CAM message interval of 100 ms.
Preserve controller frequency at 50 Hz (i.e., 20 ms).

## Slide 12: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation

## Slide 13: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
Custom Track:
• Maximum length of 6.3 m • Curvature length of 54 cm
Vehicle Model:[10]
• Length:19 cm
• Height:4.5 cm
Notes: https://carrera-toys.com/de/product/20023902-bmw-m1-procar-no5-hockenheim-1979

## Slide 14: Building The Platform
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
CPU: low-power Xtensa® 32-bit LX6 microprocessor Dual core
CPU Clock: 240 MHz
Flash memory size: 4 MB
Peripherals: UART, SPI GPIO, I2C, I2S, I2C, LED PWM, Motor PWM, USB, pulse counter, capacitive touch sensor, ADC, DAC.
Wireless connectivity: Bluetooth, BLE, Wi-Fi, and ESP-NOW
NodeMCU ESP32[11]
Defining Model Requirements
Components Selection
Software Implementation

## Slide 15: Building The Platform
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
XBee usb extension compatible
Uses UART serial communication for data sharing.
Can be used as Coordinator, Router, End Device.
Works on 2.4 GHz, and supports up to 250kbps
21 GPIOs which makes it able to work as a minor MCU
Wide supply-voltage operating range (2 V–3.6 V).
Core2530 SoC ZigBee module[12]
Defining Model Requirements
Components Selection
Software Implementation

## Slide 16: Building The Platform
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
Frame rate up to 12000 fps.
Uses SPI serial communication for data sharing.
Low latency, approximately (1 - 2) ms.
Can be easily configured to work with suitable resolution.
Acceptable velocity/acceleration up to 250 IPS/50g.
3.3V or 5V compatible
This selection was done after trials with other alternatives: Optical Shaft encoder, Reflective sensor (Groove IR, and Pololu QTR-8A)
PMW3360 Laser sensor module[13]
Defining Model Requirements
Components Selection
Software Implementation

## Slide 17: Building The Platform
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
Resolution: 2 mm.
Output type: Digital.
Low latency, approximately 1 ms.
Wide Angle: 15 degrees
Size: 45 × 21 mm.
Detection distance: 2cm-450cm
Input voltage: 5V.
Another alternative: VL53L0X ToF sensor
Distance measurement sensors[14]
Defining Model Requirements
Components Selection
Software Implementation

## Slide 18: Building The Platform
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
Supply voltage: 12 V
Supply current: 5 A
LEDMO power adaptor[15], Power Converter
Component | Voltage level (V) | Current rating (mA) | Quantity
ESP32 | 3.3 | 1200 MAX | 3
Ultrasonic | 5 | 2 | 3
PMW3360 Laser sensor | 3.3 | 23 | 3
DEV8838 Motor driver | 11 | 200 | 3
Core2530 | 3.3 | 29 MAX | 3
Summary | Total current: |  | 4360
 | Voltage levels: |  | 5,3,3,11
Defining Model Requirements
Components Selection
Software Implementation

## Slide 19: Building The Platform
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
Motor supply voltage: 0 - 11V
Motor supply current: 1.7 A Max
Carrera Motors: 18 V, and about 100 mA[17]
DRV8838 Brushed DC motor driver[16]
Defining Model Requirements
Components Selection
Software Implementation
Notes: VIKING SCALEXTRIC SLOT CAR CLUB), to

## Slide 20: Building The Platform
Car Model and Track
Microcontroller
Selecting ZigBee Module
Sensors selection:
  Speed measurements
  Distance measurements
Power Supply
Motor Driver
Logic Analyzer
8 Channels logic analyzer with capability of Analog and Digital signals capturing.
Saleae Logic 8[18]
Defining Model Requirements
Components Selection
Software Implementation

## Slide 21: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation
Communication Module
  Interface with ESP-NOW
  Mesh formation
  Send/Receive API
Relative Motion Handler Module
  Ultrasonic
  Relative motion handler algorithm
Motion Handler Module
  Laser Sensor
  Own Vehicle motion handler algorithm
PWM Module
  Motor Driver
  Motor control APIs
FreeRTOS Module
Tasks Layers

## Slide 22: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation
Communication Module
  Interface with ESP-NOW
  Mesh formation
  Send/Receive API
Relative Motion Handler Module
  Ultrasonic
  Relative motion handler algorithm
Motion Handler Module
  Laser Sensor
  Own Vehicle motion handler algorithm
PWM Module
  Motor Driver
  Motor control APIs
FreeRTOS Module
Tasks Layers

## Slide 23: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation
Communication Module
  Interface with ESP-NOW
  Mesh formation
  Send/Receive API
Relative Motion Handler Module
  Ultrasonic
  Relative motion handler algorithm
Motion Handler Module
  Laser Sensor
  Own Vehicle motion handler algorithm
PWM Module
  Motor Driver
  Motor control APIs
FreeRTOS Module
Tasks Layers

## Slide 24: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation
Communication Module
  Interface with ESP-NOW
  Mesh formation
  Send/Receive API
Relative Motion Handler Module
  Ultrasonic
  Relative motion handler algorithm
Motion Handler Module
  Laser Sensor
  Own Vehicle motion handler algorithm
PWM Module
  Motor Driver
  Motor control APIs
FreeRTOS Module
Tasks Layers

## Slide 25: Building The Platform
Communication Module
  Interface with ESP-NOW
  Mesh formation
  Send/Receive API
Relative Motion Handler Module
  Ultrasonic
  Relative motion handler algorithm
Motion Handler Module
  Laser Sensor
  Own Vehicle motion handler algorithm
PWM Module
  Motor Driver
  Motor control APIs
FreeRTOS Module
Tasks Layers
Defining Model Requirements
Components Selection
Software Implementation
Software Modules

## Slide 26: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation
Tasks layers for N_member
Communication Module
Relative Motion Handler Module
Motion Handler Module
PWM Module
FreeRTOS Module
Tasks Layers

## Slide 27: Building The Platform
Defining Model Requirements
Components Selection
Software Implementation
Tasks layers for logNode
Communication Module
Relative Motion Handler Module
Motion Handler Module
PWM Module
FreeRTOS Module
Tasks Layers

## Slide 28: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
Hardware connections

## Slide 29: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
Platform assembly process
Components preparation process

## Slide 30: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
Finally assembled platform

## Slide 31: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features

## Slide 32: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
MQTT and remote control
System Configuration File
2 D.O.F debugging
Automated Scripts
ESP-NOW Mesh and remote control communication topology

## Slide 33: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
MQTT and remote control
System Configuration File
2 D.O.F debugging
Automated Scripts
Python UI

## Slide 34: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
MQTT and remote control
System Configuration File
2 D.O.F debugging
Automated Scripts
Logged data handling

## Slide 35: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
MQTT and remote control
System Configuration File
2 D.O.F debugging
Automated Scripts
Code Snippet from System Configuration File

## Slide 36: Building The Platform
Hardware Schematic
Hardware Implementation
Additional Features
MQTT and remote control
System Configuration File
2 D.O.F debugging
Automated Scripts
Debugging
Modules’ debugging
Automated Scripts
Platoon_run.bat
Velocity_profile_parser.py
Generate_velocity_profile.m

## Slide 37: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands
Analysis preparation:
Assumptions:
  Leader vehicle velocity assumed to be constant, and a spacing error profile was estimated. This profile represents an ideal sensor measurements in analog world.
  According to the estimated profile, an estimated velocity and acceleration was also evaluated
  Error injection:
    Sensor error (1.04 – 1.1).
    Discretization.
  Assuming that the distance controller task is repeated every 10 ms
(Jeroen Ploeg, 2011)

## Slide 38: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands
Observations:
Control parameters are: Sampling interval, averaging buffer size, and sensor errors.
Optimum buffer size for velocity is 3 - 5, as for acceleration up to 20 gives promising results.
Increasing sampling frequency improves velocity profile, but acceleration profile becomes more noisy.
_________________________________________________________
Generally, the results are promising, yet needs to be verified on the Embedded target.

## Slide 39: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands

## Slide 40: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands

## Slide 41: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands

## Slide 42: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands

## Slide 43: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands
Analysis preparation:
Assumptions:
  Vehicle velocity assumed.
  According to the estimated profile, an estimated velocity and acceleration was also evaluated
  Error injection:
    Sensor error (1.04 – 1.32).
    Discretization.
  Assuming that the velocity controller task is repeated every 10 ms
(Jeroen Ploeg, 2011)

## Slide 44: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands
Observations:
Increasing the sampling interval has a huge effect for velocity estimation accuracy different than the previous test.
Acceleration requires noise filter.
Optimum average buffer size for velocity is 3 - 5, while in acceleration starts from 20..
Increasing sampling frequency improves velocity profile, but acceleration profile becomes more noisy.
_________________________________________________________
A constant shift in the velocity profile due to accumulated error in displacement measurements. As for the acceleration it shows a promising profile with 20 points average buffer size, however this comes the price of increasing computation time.

## Slide 45: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands

## Slide 46: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands

## Slide 47: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands
Test case:
2 MCUs were set to represent Leader and Vehicle One operation, One controller sends a CAM data each 100 ms, and the receiving controller sends another CAM message once a new messages is received from the leader MCU, the latency is calculated in terms of microseconds.
No. of Sent messages | No. of acks Packet | loss %
6344 | 6330 | 0.22%
Average CAM delivery: |  | 
Varies from 100 - 104 ms which is a very satisfying result |  | 
CAM message test results

## Slide 48: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands
Test case:
Distance (i.e., Ultrasonic task):
  Adding computation time for the motion analysis algorithm, the latency was in the range of (9 ms up to 16 ms)
2. Velocity (i.e., laser sensor task):
Average task latency was in range from (11 ms up to 20 ms).

## Slide 49: Platform Performance Analysis and Summary
[Simulation] Preceding Vehicle Motion Analysis
[Simulation] Motion Analysis Within The Vehicle
CAM Messages
Controller Frequency Preservation
Remote Commands
Remote control test

## Slide 50: Conclusion
Recall: Research Question
Is it possible to build a small-scale testbed giving the provided funds?
Will this model produces useful –close to real-world- results?
Is it possible to control and monitor the platform and extract data from it?
Does that model have the capability to test different platooning techniques in terms of control and communication strategies?

## Slide 51: Conclusion
Check List
Track and vehicles
MCU
Measurements and Sensors
Communication modules/protocols
Data logging
Remote control
Verification steps
Software structure and Building system

## Slide 52: Future Improvements
Sustainable CACC testbed
Hardware and wiring
Port Extended Kalman Filter (EKF)
Implement the CACC control law for each platoon member
Remote action commands
Python UI script can be improved
Streaming Camera installation
Major Improvements
Estimation Algorithms
Minor Improvements
Software architecture
Dedicated IMU sensor

## Slide 53
Thank you! Questions?